Ghost circa 1920 when located on firewall with ballast incorporated below – note narrow raised section in cap  Note wide section in cap below to allow access space for 2 wires.  Both caps have brass insert. 
Note brass inserts at bolt holes. Main case is ‘stabilite’ by Mouldenite Manufacturing Co but cap & knobs are ‘bakelite’.   ‘Bakelite’ coil with R-R inscription is shown in John Fasal’s ‘Twenty’ book  on p.158 & p.160 – this is considered to be pre-production and appears not to have been used in production. 
Note :  central rod passes completely thru coil with large washer & nut countersunk in base.

Replica   made in USA & supplied by Rudy Rosales

20hp mascot  adjacent to late 1923 Squat style (Note knob location –this one supplied when coil moved to front timing case);  Centre coil is late 1924 to late 1926;  1927 (Series ‘J’) onwards (note change from ‘stabilite’ to ‘bakelite’ case).  Internal plates and nuts are unplated brass but are nickel plated by c1930.  
The colour difference in the first two coils is due to oil contamination.
Each square base coil is stamped with number on one side of the base by the Electrical Department.