Age and Authenticity

Footpumps supplied with Twenty HP

Can anyone add information to my following observations?

The 1924 List of Parts book shows a diagram of the footpump supplied stating it is a Dunlop brand.

I have noted an early original chassis which was supplied with a ‘Mortier Deluxe’ footpump and it is definitely identical to the Parts Book sketch.  Was ‘Mortier’ a subsidiary of Dunlop or was the ‘Mortier’ changed to ‘Dunlop’ in early 1924?

As there are very few cars in Australia that are quite original and still have substantial numbers of their original toolkits and have not been ‘restored’, I have been unable to ascertain if the  ‘Dunlop’ was ever supplied and which model ‘Dunlop’ pump was supplied.  The 1925 Ghost LoP also shows the Mortier pump, it is therefore likely that the Dunlop pump was never supplied in the 1920’s.

Although not shown nor mentioned in the 1924 and 1928 Supplement, it appears that the footpump supplied was changed to the “ Kismet Junior” in 1925 and continued thru until at least mid 1927  (still fitted to Series J chassis GAJ26 and GAJ32).  It is shown as supplied with the New Phantom and is shown in the 1925 Phantom Parts book but with a 20hp part number.

The 1928 Parts Supplement shows that a ‘Nesthill’ footpump was supplied by 1928 and used thru into the 1930’s..

I have noted that some owners are over restoring their cars by fitting both the double ended open–end spanners and the single ended jaw spanners.  It appears that only 1923 Series ‘A’ chassis were supplied with the double ended spanners (F6372, 9799, F2894, F9881).  This is stated in the 1928 Supplement.

Quite often, the 1928 Supplement must be used in conjunction with the 1924 LoP to decide the correct part.

Early chassis were also supplied with a  6” copper petrol funnel up to at least the GF series chassis.

Part numbers

A new series of part numbers was commenced for the Twenty, these commenced at F50000 (chassis side member) and went thru into the 55000 series.  20/25 chassis numbers appear to commence about 56000.  These numbers were prefixed with F for Frame parts, D for Electrical parts, G for Gearbox, and E for Engine parts.  New Phantom part numbers are 70000 series and PII appear to be 80000 series.  Of course, the Twenty being so good, parts from the Twenty were migrated to the larger 40/50 chassis.  The major example would be the Distributor mechanism.