SERVICE INSTRUCTION LEAFLET RR/V,.

.

(B) Rear Hubs. 	,

Refer to Fig. 6.

* 1.  Push in the chromium plated sliding barrel (0) 
against the spring (P) behind it, and prise out 
the spring retaining ring (Q) by means of a 
screwdriver inserted in one of the two slots in 
the hub. The sliding barrel and spring can now be 
removed.

2.  By means of a screwdriver remove the wire lock

ring (R) from inside the grease cap retaining
nut (S) and unscrew the nut with the special 
spanner. Remove the grease cap (T). Note:- The 
nut is right hand thread on both sides.

3.  Remove the split pin and unscrew the axle

shaft nut (U). In addition to the plain washer, 
(V) there may be a packing washer (V) fitted be- 
hind the nut and special note must be made of 
this in order that it is not forgotten when re- 
assembling. Note:- The nut is right hand thread 
on both sides.

4. 	Withdraw the driving dog (W) by screwing in with the

extractor 2 x threaded rods G8522.

5. 	Remove the three 2BA nuts and spring washers

that hold the locking plate (X) to the axle tube 
nut (Y) and remove the locking plate.

6. 	Unscrew the axle tube nut with the special

spanner.  Note:- The thread is left hand on the 
near (kerb) side and right hand on the off side.

7. 	Withdraw the hub with the special extractor.

* Operation 1 does not apply to the Wraith.

The Wraith grease retaining cap screws into the hub 
It has no locking piece and can be removed with a 
box spanner on its hexagon head. Note:- The thread 
is right hand on both sides.